Universal Magnetic Swipe Reader PC Keyboard Interface The Universal Magnetic Swipe Reader can read any combination of up to three tracks of magnetic information with a single swipe in either direction. An audible tone and a visual LED signal indicate a successful read. The Universal Magnetic Swipe Reader accepts both high and low coercivity magnetic cards, and can read all ISO 7811, AAMVA and California Driver's license, and custom data formats. Programmability options allow the user to select different languages and output data format, including divide, rearrange, edit, and validate fields of magnetic card data. The unique optional dual head configuration can read a magnetic stripe without requiring the user to orient the stripe in a specific direction. The Universal Magnetic Stripe Reader can be used as a freestanding unit; Velcro mounted or permanently mounted using two screws. There are several interfaces to choose from including, PC Keyboard, USB keyboard emulation, USB RS232 emulation, Serial RS-232. There is no external power supply needed. The available color choices are Beige and Black FEATURES Small Footprint - can be mounted on keyboard or any flat surface Bi-directional swipe Decodes Up to Any combination of three tracks ISO, AAMVA and DMV Compliant Reads both credit cards and Driver Licenses (AAMVA and California Standard) No special software or drivers need Keyboardless feature lets the reader work with most Laptops without external keyboard User-friendly setup via keyboard LED and Buzzer indicators Programmable audio response Programmable data output 500K Magnetic Head Life FCC class A Part 15 and CE Mark Class A One-Year Warranty Firmware downloadable SPECIFICATIONS Recording Method Two-frequency coherent phase (F2F), compatible with ISO 7811 and AAMVA Swipe Speed 5 to 55 in/sec, (127 to 1400 mm/Sec) Power Consumption 70mA Communication Keyboard simulator interface Operating Temp - 10°C to + 50°C Storage Temp -30°C to +70°C Operating Humidity 10-85% (non condensing) Storage Humidity 10-90% (non condensing) Magnetic Head Life 500K swipes min, (1M optional) Weight 208g (7.0oz) Dimensions 100L x 34W x 27H mm (3.94L x 1.34W x 1.10H inches) OUTPUT DATA FORMAT: Single track <SS><TRACK1 or 2 or 3 DATA><ES><CARRIAGE RETURN> Dual track <SS><TRACK1 or 2 DATA><ES><CARRIAGE RETURN> <SS><TRACK2 or 3 DATA><ES><CARRIAGE RETURN> Triple track <SS><TRACK1 DATA><ES><CARRIAGE RETURN> <SS><TRACK2 DATA><ES><CARRIAGE RETURN> <SS><TRACK3 DATA><ES><CARRIAGE RETURN> Remarks: SS = START SENTINEL TRACK1= "%" (ISO, DMV & AAMVA) TRACK2= ";" (ISO, DMV & AAMVA) TRACK3= ";" (ISO) "%" (AAMVA) "!" (CA old DMV) ES = END SENTINEL TRACK1, 2 & 3= "?" (ISO, CA old DMV & AAMVA) Specifications are subject to change without notice. All brand names and registered trademarks are the property of their owners. Part No. KIT Contents ZAUM100-KB Universal Magnetic Swipe Reader, Single Track, Track 1, PC Keyboard Interface, Beige ZAUM100-KL Universal Magnetic Swipe Reader, Single Track, Track 1, PC Keyboard Interface, Black ZAUM020-KB Universal Magnetic Swipe Reader, Single Track, Track 2, PC Keyboard Interface, Beige ZAUM020-KL Universal Magnetic Swipe Reader, Single Track, Track 2, PC Keyboard Interface, Black ZAUM003-KB Universal Magnetic Swipe Reader, Single Track, Track 3, PC Keyboard Interface, Beige ZAUM003-KL Universal Magnetic Swipe Reader, Single Track, Track 3, PC Keyboard Interface, Black ZAUM120-KB Universal Magnetic Swipe Reader, Dual Tracks, Tracks 1&2, PC Keyboard Interface, Beige ZAUM120-KL Universal Magnetic Swipe Reader, Dual Tracks, Tracks 1&2, PC Keyboard Interface, Black ZAUM103-KB Universal Magnetic Swipe Reader, Dual Tracks, Tracks 1&3, PC Keyboard Interface, Beige ZAUM103-KL Universal Magnetic Swipe Reader, Dual Tracks, Tracks 1&3, PC Keyboard Interface, Black ZAUM023-KB Universal Magnetic Swipe Reader, Dual Tracks, Tracks 2&3, PC Keyboard Interface, Beige ZAUM023-KL Universal Magnetic Swipe Reader, Dual Tracks, Tracks 2&3, PC Keyboard Interface, Black ZAUM123-KB Universal Magnetic Swipe Reader, Three Tracks, 1,2&3, PC Keyboard Interface, Beige ZAUM123-KL Universal Magnetic Swipe Reader, Three Tracks, 1,2&3, PC Keyboard Interface, Black