Point to Multi-point Bluetooth Module

User’s manual

Table of Contents

1.	Summary	4

2.	Data Interface	4

2.1.	Communication Protocol	4

2.2.	Command Frame:	5

2.3.	Command Set	6

2.3.1.	Set/Inquire baud-rate	6

2.3.2.	Set/Inquire communications parameters	6

2.3.3.	Set/Inquire Hardware Handshake flow control	7

2.3.4.	Set/Inquire Authentication	7

2.3.5.	Set/Inquire BT Module name	7

2.3.6.	Set/Inquire BT Module class	8

2.3.7.	Clearing all connected remote Bluetooth devices address	8

2.3.8.	Set/Inquire Sniff configuration	8

2.3.9.	Reset Module to default parameters	8

2.3.10.	Set/Inquiry Scan Time	8

2.3.11.	Inquire Modules firmware version	9

2.3.12.	Inquire remote BT address	9

2.3.13.	Inquire local device BT address	9

2.3.14.	Soft-reboot of the module	10

2.3.15.	Commence Discovery process	10

2.3.16.	Cancel the discovery process	10

2.3.17.	Set/ Inquire PIN code mode	10

2.3.18.	Set /Inquire PIN (password) number	11

2.3.19.	Pair with remote Bluetooth Device	11

2.3.20.	Unpair a remote device that is currently paired.	11

2.3.21.	Connect Remote Bluetooth device	11

2.3.22.	Disconnect Remote Bluetooth Device	12

2.3.23.	Inquire Current Connection status	13

2.3.24.	Mode switch	13

2.3.25.	LED operational Mode indicators	14

2.3.26.	Module start instruction	14

2.3.27.	Inquire available AT instructions	14

2.4.	Data packet Format (0x10 )	14

2.5.	Data packet reply (0x20)	16

3.	Examples of the various User Procedures	17

3.1.	Bluetooth Module Discovery Inquiry	17

3.1.1.	Commence the discovery process for remote BT devices	17

3.1.2.	Cancel the discovery process	17

3.2.	Communication Protocol example to pair two devices	18

3.3.	Initiative connection serial port service flow	20

3.4.	Serial port data transmission flow	20

3.4.1.	Transmitting HelloWorld	20

3.4.2.	Disconnecting serial port service	20

4.	Bluetooth Module Hardware	21

5.	Document Status & Contact Information	22

# Summary

The following document describes the operation of a Point to Multi-Point Bluetooth Data module supporting up to 4 Bluetooth devices forming a Piconet connection.

# Data Interface

To achieve The multi-point Bluetooth Module firmware has been designed to receive data in a very specific format. The requirements of forming a Piconet and properly mapping the data to the correct microprocessor follows very strict formatting, especially for the AT commands structure and as well as the modules data. Communication packets not adhering to the required format will be regarded as invalid data.

## Communication Protocol

The host microcontroller should be connected to the Bluetooth Modules via UART connection. The default communication parameters are 115200bps, Hardware Handshake (RTS/CTS) 8 bits, 1 stop, no parity.

All communication between the Host controller and Bluetooth module must follow the outlined communication format.

There are two types of communication formats

- Command format and

- Data frame.

## Command Frame:

AT command format from MCU to Module

| Prefix | Header type | Data length | Application data | Suffix |
| --- | --- | --- | --- | --- |
| 0x55 | 0xAA | 0x(00）（2Byte） | （0 - 65535）Bytes | 0x0D | 0x0A |  |

AT command response from Module to MCU:

| Prefix | Header type | Data Length | Data prefix | Data | Suffix |
| --- | --- | --- | --- | --- | --- |
| 0x0D | 0x0A | 0x01 | 2 bytes | 0x0D | 0x0A | (0-65535) Bytes | 0x0D | 0x0A |

Note:

1. The length includes Data Prefix and Suffix.

2. The length are two byte with high byte first

3. The length byte is Hex format

Example of Bytes for Data length = 258

The two bytes of length bytes = 0x01, 0x02

The Following example is used to show how the authentication would be set:

Set Authentication

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+AUTH=1 | OK | <flag>： 0: Authentication disabled 1: Authentication disabled Default mode: Authentication Enabled |

MCU to Module:

| 0x55 | 0xAA | 0x00 | 0x00 | 0x0b | 0x41 | 0x54 | 0x2b | 0x41 | 0x55 | 0x54 | 0x48 | 0x3D | 0x31 | 0x0d | 0x0a |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Prefix1 | Prefix2 | AT command | Data length High | Data length low | A | T | + | A | U | T | H | = | 1 | Suffix1 | Suffix 2 |

Response from Module

| 0x55 | 0xAA | 0x01 | 0x00 | 0x06 | 0x0D | 0x0A | 0x4F | 0x4B | 0x0D | 0x0A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Prefix1 | Prefix2 | Header as AT command | Data length High | Data length low | Data prefix 1 | Data Prefix 2 | O | K | Suffix 1 | Suffix 2 |

## Command Set

### Set/Inquire baud-rate

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+BAUD=< baud> | OK | baudrate：(1200、2400、4800、9600、19200、38400、57600、115200、230400、460800、921600、1382400） Default: 115200 |
| AT+BAUD？ | OK ＋BAUD:< baud > |  |

### Set/Inquire communications parameters

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+UARTMODE=<stopbit>, <paritybit> | OK | <stopbit> 0：1 Stop bit 1：2 Stop bits <parity bit> 0：NO Parity 1：ODD 2：Even Default: One (1) Stop bit and parity = none |
| AT+ UARTMODE? | OK ＋UARTMODE: <stop bit>,<parity bit> |  |

### Set/Inquire Hardware Handshake flow control

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+FLOWCONTROL=<flag> | OK | <flag>： 0：No hardware handshake 1：Hardware handshake CTS/RTS enabled Default = hardware handshake enable |
| AT+FLOWCONTROL? | ＋FLOWCONTROL: <flag> |  |

### Set/Inquire Authentication

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+AUTH=< flag> | OK | <flag>： 0: Authentication disabled 1: Authentication disabled Default mode: Authentication Enabled |
| AT+AUTH？ | OK ＋AUTH:<flag> |  |

### Set/Inquire BT Module name

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+NAME=<name> | OK | Module name |
| AT+NAME？ | OK ＋NAME:<name> |  |

### Set/Inquire BT Module class

| 指令 | Response from Module | Parameter |
| --- | --- | --- |
| AT+CLASS=<classofdevice> | OK | Class ( length is fixed at 6 bytes) Default =000000 |
| AT+CLASS？ | OK ＋CLASS: < classofdevice > |  |

### Clearing all connected remote Bluetooth devices address

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CLEARADDR | OK | None |

### Set/Inquire Sniff configuration

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+SNIFF=<maxtime>, <mintime>,<try>,<timeout> | OK | maxtime： mintime： sniff interval： timeout： Default=200,32,1,8 |
| AT+SNIFF？ | OK ＋SNIFF:<maxtime>, <mintime>,<try>,<timeout> |  |

### Reset Module to default parameters

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+RESET | OK | None |

### Set/Inquiry Scan Time

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+SCANTIME=<pageinterval>,<pagewindow>,<inqinterval>, <inqwindow> | OK | If < pageinterval> = 0 then the module will not respond to any page. No connection can be made. If < pagewindowl> = 0 then the module will not respond to any page. No connection can be made. If <inqinterval> = 0 then the module will not respond to any inquiry. No connection can be made. If <inqwindow> = 0 then the module will not respond to any inquiry. No connection can be made. Default 2048,18,2048,18 |
| AT+SCANTIME？ | OK ＋SCAN:<pageinterval>, <pagewindow>,<inqinterval>,<inqwindow> |  |

### Inquire Modules firmware version

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+VERSION？ | OK ＋VERSION:<version> | Firmware version |

### Inquire remote BT address

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+ RADDR? | OK ＋RADDR:<bdaddr> | Max connected BT device is 7 |

### Inquire local device BT address

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+LADDR？ | OK ＋LADDR:<bdaddr> | Bdaddr: is the Bluetooth Device address of the local module |

### Soft-reboot of the module

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+ RESTART | OK |  |

### Commence Discovery process

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+INQ | OK Inquiry result: +INQRESU:<bdaddr>, <name> Inquiry complete： +INQCOMP | < bdaddr >BT address of the discovered Bluetooth device <name> Friendly name of the discovered Bluetooth device. (Note:If a name is not found then “Unknown” is returned) |

### Cancel the discovery process

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CANCEL | OK |  |

### Set/ Inquire PIN code mode

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+PINMODE=<flag> | OK | <flag>： 1: Use default PIN Response（doesn’t not send PINRES command） 0: Send PINRES Command） Default=0 |
| AT+PINMODE? | OK +PINMODE:<flag> | Pinmode Inquiry |

### Set /Inquire PIN (password) number

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+PASSWORD=<pin> | OK | <pin>：PIN number Default=0000 |
| AT+PASSWORD? | OK +PASSWORD:<pin> | <pin>: returns the current PIN # |

### Pair with remote Bluetooth Device

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+PAIR=<bdaddr> | OK | <bdaddr>Bluetooth Address <pin>PasswordPassword <Status> l: Success 0: Failure |
|  | +PININD: <bdaddr> |  |
| AT+PINRES=<bdaddr>,<pin> |  |  |
|  | +PAIR: <bdaddr>, <Status> |  |

### Unpair a remote device that is currently paired.

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+DEL=<bdaddr> | OK | <bdaddr> |

### Connect Remote Bluetooth device

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CONN=<bdaddr>, <service> | OK | <bdaddr>Blue tooth address <service> Device type 0x1101 SPP 0x1108 Headset |
|  | +CONN:<handle>,<bdaddr>, <service>,<state> | <handle>device ID Note: This device ID will be assigned after successful connection <bdaddr> <service>Device type <Status> : 0: Successfully connected 1: Can’t make connection/interrupted 2: Can’t not obtained Bluetooth device service type 3: Can’t pair |

### Disconnect Remote Bluetooth Device

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+DISC=<handle> | OK | <handle>Device ID |
|  | +CONN:<handle>,<bdaddr>, <service>,<state> | <handle> the device ID only will be signed after successful connection <bdaddr> BDADDRESS <service> Device Type <status>： 0: Successfully connected 1: Can’t make connection/interrupted 2: Can’t not obtained Bluetooth device service type 3: Can’t pair |

### Inquire Current Connection status

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CONN? | OK +CONN: handle>,<bdaddr>, <service>,<status> | None Return current status. |

### Mode switch

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+MASTER=switch_mode | OK | switch_mode： 0 no Change 1: Switch to Master. If cannot switch to master, disconnect from remote device 2: Switch to Master, If cannot make the switch, stay connected Default = 2 |
| AT+MASTER? | OK +MASTER: switch_mode | Current status。 |

### LED operational Mode indicators

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+LED=spp_ind | OK | spp_ind: SPP（0-11）Connection LED indicating lamp disposition. (0-11) |
| AT+LED? | OK +LED: spp_ind |  |

### Module start instruction

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+OPEN：paired_num | NONE | paired_num: Report connected number of devices |

### Inquire available AT instructions

| Command | Response from Module | Parameter |
| --- | --- | --- |
| ATZ? | OK List then available AT instructions | None |

## Data packet Format (0x10 )

The data packet is formatted as follows:

- The first three bytes are fixed

- The next two bytes are indicative of the packet length

- The next two bytes are the destination header

- The remainder is the payload data which is two bytes less than the designated length

The following is an example of the Data communication format

| Fixed Header | Designator for data | Data length | Destination ID | Data |
| --- | --- | --- | --- | --- |
| 0x55 | 0xAA | 0x10 | Data length (2 bytes) | （2bytes) | application payload (length – 2bytes） |

The first three bytes are fixed as:  0x55 0xAA 0x10

The data length of two bytes includes the two bytes it needs to define the destination ID.

The Destination ID: 2 bytes in length and is returned when the device connects to a remote Bluetooth device. The destination ID is used to determine which device in the Piconet will receive the data.

Payload: this is the application data. The length of the data packet is its length reduce from the transmit length by two (2) bytes.

For example:

After connecting successfully, the module returns:

+CONN:1232,4A494E000067,1101,0

The connection destination ID is the 4A494E000067

The remote BT device corresponds to the 1232 (16 bits address)

If you choose to transmit the string of characters “HelloWorld” to the address is the 4A494E000067 equipment:

Then you will transmit “55 AA 10 00 0C 12 32 48 65 6C 6C 6F 57 6F 72 6C 64”

The data in Black = 55 AA 10 00 0C is the prefix and the data length (0x0C is the length)

The data in Blue = 12 32 is the destination ID

The data in Red = 48 65 6C 6C 6F 57 6F 72 6C 64 is Hello World

Please note: When transmitting large amounts of Data it is recommended that the system use Hardware Handshaking. This will help insure the reliability of the data in the Piconet. If for some reason hardware handshaking cannot be implemented the we recommend that the payload be limited to 400 bytes of data, Additionally  the data transmitting microprocessor should wait for an acknowledgement that the data was received properly before transmitting the next batch.

## Data packet reply (0x20)

The Reply to receiving a data packet is described below the receive data packet is distinguished by the 0x20 in the third byte position:

| 0x55 | 0xAA | 0x20 | Data Length | Object code (1 byte | Destination ID (2 bytes) |
| --- | --- | --- | --- | --- | --- |

Object code Table

| Object code | Result description |
| --- | --- |
| 0x00 | Correct reply |
| 0x01 | Data packet error: Undefined packet type. |
| 0x02 | Packet length invalid (2<= N <=65535） |
| 0x03 | Data packet transmission time surpasses for 5 seconds |
| 0x04 | Invalid destination ID: If the Module receives a Data packet without a destination ID then the module will automatically substitute a default value of “00” |

If returns = 55 AA 20 00 03 04 12 34 then the 0x04 in the object code location is indicative of the fact that the Destination ID 1234 is invalid.

# Examples of the various User Procedures

## Bluetooth Module Discovery Inquiry

### Commence the discovery process for remote BT devices

#### uP to module ( AT+INQ<CR><LF>）

#### 55 AA 00 00 08 41 54 2B 49 4E 51 0D 0A

#### Module to uP Response ( <CR><LF>OK<CR><LF>

55 AA 01 00 06 0D 0A 4F 4B 0D 0A

#### Result of the INQ command

#### Module to uP Response (（<CR><LF>+INQRESU:addr,name<CR><LF>）

Example hex response to a module with address: name =:001B3502BC8B, BTM0102C2P

55 AA 01 00 24 0D 0A 2B 49 4E 51 52 45 53 55 3A 30 30 31 42 33 35 30 32 42 43 38 42 2C 42 54 4D 30 31 30 32 43 32 50 0D 0A

Example hex response to a module with  address:name =:001B35025C4A ,BTM0102C2P

55 AA 01 00 24 0D 0A 2B 49 4E 51 52 45 53 55 3A 30 30 31 42 33 35 30 32 35 43 34 41 2C 42 54 4D 30 31 30 32 43 32 50 0D 0A

### Cancel the discovery process

#### uP to module ( (AT+CANCEL<CR><LF>)

55 AA 00 00 0B 41 54 2B 43 41 4E 43 45 4C 0D 0A

- Module to uP Response ( (<CR><LF>OK<CR><LF>)

55 AA 01 00 06 0D 0A 4F 4B 0D 0A

Inquiry completed

- Module to uP Response ( (<CR><LF>+INQCOMP<CR><LF>)

55 AA 01 00 0C 0D 0A 2B 49 4E 51 43 4F 4D 50 0D 0A

## Communication Protocol example to pair two devices

The following is an example of the communication flow that is typically followed when attempting to pair two devices. In this example the remote Bluetooth device has the following BT address: 001B3502BC8B) Note: all of the commands uP to module have a prefix of 0x55 0xAA

Designator byte and data length

- The host processor will send the following command to the BT module:

uP to Module ( (AT+PAIR=001B3502BC8B<CR><LF>)

55 AA 00 00 16 41 54 2B 50 41 49 52 3D 30 30 31 42 33 35 30 32 42 43 38 42 0D 0A

- And the response from the BT module

Module to uP Response ( <CR><LF>OK<CR><LF>)

55 AA 01 00 06 0D 0A 4F 4B 0D 0A

- The following is the PIN # instructions:

Module to uP Response ( (<CR><LF> +PININD: 001B3502BC8B<CR><LF>)

The remote device receives (<CR><LF> +PININD: 001B3502BC8A<CR><LF>)

55 AA 01 00 18 0D 0A 2B 50 49 4E 49 4E 44 3A 30 30 31 42 33 35 30 32 42 43 38 42 0D 0A

55 AA 01 00 18 0D 0A 2B 50 49 4E 49 4E 44 3A 30 30 31 42 33 35 30 32 42 43 38 41 0D 0A

- Response to the Password Inquiry （Password:1234）

  - Module to uP Response ( (AT+PINRES=001B3502BC8B,1234 <CR><LF>)

The remote device sends out (AT+PINRES=001B3502BC8A,1234 <CR><LF>)

55 AA 00 00 1D 41 54 2B 50 49 4E 52 45 53 3D 30 30 31 42 33 35 30 32 42 43 38 42 2C 31 32 33 34 0D 0A

55 AA 00 00 1D 41 54 2B 50 49 4E 52 45 53 3D 30 30 31 42 33 35 30 32 42 43 38 41 2C 31 32 33 34 0D 0A

Module to uP Response ( (CR><LF>OK CR><LF>)

55 AA 01 00 06 0D 0A 4F 4B 0D 0A

- Successfully paired

Module to uP Response ( (<CR><LF> +PAIR: 001B3502BC8B,1 <CR><LF>)

Module to uP Response ( (<CR><LF>+PAIR: 001B3502BC8A,1 <CR><LF>)

55 AA 01 00 18 0D 0A 2B 50 41 49 52 3A 30 30 31 42 33 35 30 32 42 43 38 42 2C 31 0D 0A

55 AA 01 00 18 0D 0A 2B 50 41 49 52 3A 30 30 31 42 33 35 30 32 42 43 38 41 2C 31 0D 0A

## Initiative connection serial port service flow

- The commands to inquire a remote connection

uP to Module (（AT+CONN=001B3502BC8B,1101<CR><LF>）

55 AA 00 00 1B 41 54 2B 43 4F 4E 4E 3D 30 30 31 42 33 35 30 32 42 43 38 42 2C 31 31 30 31 0D 0A

Module to uP ( （<CR><LF>OK<CR><LF>)

55 AA 01 00 06 0D 0A 4F 4B 0D 0A

- Upon successfully connecting

- Module to uP ( (<CR><LF>+CONN:1010,001B3502BC8B,1101,0<CR><LF>)

- 55 AA 01 00 22 0D 0A 2B 43 4F 4E 4E 3A 31 30 31 30 2C 30 30 31 42 33 35 30 32 42 43 38 42 2C 31 31 30 31 2C 30 0D 0A

## Serial port data transmission flow

### Transmitting HelloWorld

This example makes the assumption that the remote ID is 0x1232.

uP to Module ( (HelloWorld)

uP to Module ( 55 AA 10 00 0C 12 32 48 65 6C 6C 6F 57 6F 72 6C 64

Module to uP (  55 AA 20 00 03 12 32

The remote module will receive (48 65 6C 6C 6F 57 6F 72 6C 64

Remote modules will reply with the addition of the Destination ID (0x1232)

55 AA 10 00 0C 12 36 48 65 6C 6C 6F 57 6F 72 6C 64

### Disconnecting serial port service

Disconnect remote Bluetooth equipment

uP to Module (  (AT+DISC=1010 <CR><LF>)

55 AA 00 00 0E 41 54 2B 44 49 53 43 3D 31 30 31 30 0D 0A

Module to uP (  (<CR><LF>OK<CR><LF>)

55 AA 01 00 06 0D 0A 4F 4B 0D 0A

Disconnection instruction

Module to uP (  (<CR><LF>+CONN=1010,001B3502BC8B,1101,1<CR><LF>)

55 AA 01 00 1D 0D 0A 2B 43 4F 4E 4E 3D 30 30 31 42 33 35 30 32 42 43 38 42 2C 31 31 30 31 2C 31 0D 0A

# Bluetooth Module Hardware

The Point to multipoint Bluetooth firmware described in this document can be used with the following modules:

- BT44-191C Data communication only

- BT44-191S Data and Audio

- BT44-147 Data and Audio

- BT44-111S Data and Audio

Note1; the above communication flow has been described in detail for a a Bluetooth Module operating as a MASTER SPP (Serial Port Profile) device.  The Module would be able to connect to any Bluetooth slave device that has the SPP profile.

Note 2: For audio applications please contact ZBA for additional details and requirements for operating as a Bluetooth MASTER with point to multipoint function and transmitting audio data.

# Document Status & Contact Information

| Date | Comments |
| --- | --- |
| April 2009 | First draft |

To make a request for change, correction, additions or information on references, please contact:

ZBA, Inc. 
94 Old Camplain Road 
Hillsborough, NJ   08844
Phone: 908-359-2070

Fax 908-595-0909

E-mail: techsupport@zbausa.com

Website : http://www.bluetoothmodules.net

# Text boxes

001B3502BC8A

001B3502BC8B

Bluetooth Module

Host uP

Bluetooth Module

Host uP