Point to Multi-point Bluetooth Module

User’s manual

Table of Contents

1.	Summary	3

2.	Data Interface	3

3.	Communication Protocol	4

3.1.	Command Frame:	5

3.2.	Command Set:	7

3.2.1.	Set/Inquire baud-rate	7

3.2.2.	Set/Inquire communications parameters	7

3.2.3.	Set/Inquire Hardware Handshake flow control	8

3.2.4.	Set/Inquire Authentication	8

3.2.5.	Set/Inquire BT Module name	8

3.2.6.	Set/Inquire BT Module class	9

3.2.7.	Clearing all connected remote Bluetooth devices address	9

3.2.8.	Set/Inquire Sniff configuration	9

3.2.9.	Reset Module to default parameters	9

3.2.10.	Set/Inquiry Scan Time	10

3.2.11.	Inquire Modules firmware version	10

3.2.12.	Inquire remote BT address	10

3.2.13.	Inquire local device BT address	11

3.2.14.	Soft-reboot of the module	11

3.2.15.	Commence Discovery process	11

3.2.16.	Cancel the discovery process	11

3.2.17.	Set/ Inquire PIN code mode	11

3.2.18.	Set /Inquire PIN (password) number	12

3.2.19.	Pair with remote Bluetooth Device	12

3.2.20.	Unpair a remote device that is currenlty paired.	13

3.2.21.	Connect Remote Bluetooth device	13

3.2.22.	Disconnect Remote Bluetooth Device	14

3.2.23.	Inquire Current Connection status	14

3.2.24.	Mode switch	15

3.2.25.	LED operational Mode indicators	15

3.2.26.	Module start instruction	16

3.2.27.	Inquire available AT instructions	16

3.3.	Data packet Format（0x10）	16

3.4.	Data packet reply (0x20)	17

4.	Examples of the various User Procedures	19

4.1.	Bluetooth Module Discovery Inquiry	19

4.2.	Communication Protocol example to pair two devices	20

4.3.	Initiative connection serial port service flow	21

4.4.	Serial port data transmission flow	22

4.4.1.	Transmitting HelloWorld	22

4.4.2.	Disconnecting serial port service	22

5.	Bluetooth Module Hardware Specification	23

# Summary

The following document describes the operation of a  Point to Multi-Point Bluetooth Data module supporting up to 4 Bluetooth devices forming a Piconet connection.

# Data Interface

To achieve The multi-point Bluetooth Module firmware has been designed to receive data in a very specific format. The requirements of forming a piconet and properly mapping the data to the correct microprocessor follows very strict formatting, especially for the AT commands structure and as well as the modules data. Communication packets not adhering to the required format will be regarded as invalid data.

## Communication Protocol

The host microcontroller should be connected to the Bluetooth Modules via UART connection. The default communication parameters are 115200bps, Hardware Handshake (RTS/CTS) 8 bits, 1 stop, no parity.

All communication between the Host controller and Bluetooth module must follow the outlined communication format.

There are two types of communication formats

- Command format and

- Data frame.

## Command Frame:

AT command format from MCU to Module

| Prefix | Header type | Data length | Application data | Suffix |
| --- | --- | --- | --- | --- |
| 0x55 | 0xAA | 0x(00）（2Byte） | （0 - 65535）Bytes | 0x0D | 0x0A |  |

AT command response from Module to MCU:

| Prefix | Header type | Data Length | Data prefix | Data | Suffix |
| --- | --- | --- | --- | --- | --- |
| 0x0D | 0x0A | 0x01 | 2 bytes | 0x0D | 0x0A | (0-65535) Bytes | 0x0D | 0x0A |

Note:

1. The length includes Data Prefix and Suffix.

2. The length are two byte with high byte first

3. The length byte is Hex format

Example of Bytes for Data length = 258

The two bytes of length bytes = 0x01, 0x02

The Following example is used to show how the authentication would be set:

Set Authentication

| Command | Response from Module | Paramter |
| --- | --- | --- |
| AT+AUTH=1 | OK | <flag>： 0: Authentication disabled 1: Authentication disabled Default mode: Authentication Enabled |

MCU to Module:

| 0x55 | 0xAA | 0x00 | 0x00 | 0x0b | 0x41 | 0x54 | 0x2b | 0x41 | 0x55 | 0x54 | 0x48 | 0x3D | 0x31 | 0x0d | 0x0a |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Prefix1 | Prefix2 | AT command | Data length High | Data length low | A | T | + | A | U | T | H | = | 1 | Suffix1 | Suffix 2 |

Response from Module

| 0x55 | 0xAA | 0x01 | 0x00 | 0x06 | 0x0D | 0x0A | 0x4F | 0x4B | 0x0D | 0x0A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Prefix1 | Prefix2 | Header as AT command | Data length High | Data length low | Data prefix 1 | Data Prefix 2 | O | K | Suffix 1 | Suffix 2 |

## Command Set:

### Set/Inquire baud-rate

| Command | Response from Module | Paramter |
| --- | --- | --- |
| AT+BAUD=< baud> | OK | baudrate：(1200、2400、4800、9600、19200、38400、57600、115200、230400、460800、921600、1382400） Default: 115200 |
| AT+BAUD？ | OK ＋BAUD:< baud > |  |

### Set/Inquire communications parameters

| Command | Response from Module | Paramter |
| --- | --- | --- |
| AT+UARTMODE=<stopbit>, <paritybit> | OK | <stopbit> 0：1 Stopbit 1：2 Stopbits <paritybit> 0：NO Parity 1：ODD 2：Even Default: One (1) Stop bit and parity = none |
| AT+ UARTMODE? | OK ＋UARTMODE: <stopbit>,<paritybit> |  |

### Set/Inquire Hardware Handshake flow control

| Command | Response from Module | Paramter |
| --- | --- | --- |
| AT+FLOWCONTROL=<flag> | OK | <flag>： 0：No hardware handshake 1：Hardware handshake CTS/RTS enabled Default = hardware handshake enable |
| AT+FLOWCONTROL? | ＋FLOWCONTROL: <flag> |  |

### Set/Inquire Authentication

| Command | Response from Module | Paramter |
| --- | --- | --- |
| AT+AUTH=< flag> | OK | <flag>： 0: Authentication disabled 1: Authentication disabled Default mode: Authentication Enabled |
| AT+AUTH？ | OK ＋AUTH:<flag> |  |

### Set/Inquire BT Module name

| Command | Response from Module | Paramter |
| --- | --- | --- |
| AT+NAME=<name> | OK | Module name |
| AT+NAME？ | OK ＋NAME:<name> |  |

### Set/Inquire BT Module class

| 指令 | Response from Module | Parameter |
| --- | --- | --- |
| AT+CLASS=<classofdevice> | OK | Class ( length is fixed at 6 bytes) Default ：000000 |
| AT+CLASS？ | OK ＋CLASS: < classofdevice > |  |

### Clearing all connected remote Bluetooth devices address

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CLEARADDR | OK | None |

### Set/Inquire Sniff configuration

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+SNIFF=<maxtime>, <mintime>,<try>,<timeout> | OK | maxtime： mintime： sniff interval： timeout： Default：200,32,1,8 |
| AT+SNIFF？ | OK ＋SNIFF:<maxtime>, <mintime>,<try>,<timeout> |  |

### Reset Module to default parameters

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+RESET | OK | None |

### Set/Inquiry Scan Time

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+SCANTIME=<pageinterval>,<pagewindow>,<inqinterval>, <inqwindow> | OK | Page interval If page interval = 0 It will not response any page. No connection can be made. Pagewindow inqinterval：0 It will not response any inquiry. No connection can be made inqwindow： Default 2048,18,2048,18 |
| AT+SCANTIME？ | OK ＋SCAN:<pageinterval>, <pagewindow>,<inqinterval>,<inqwindow> |  |

### Inquire Modules firmware version

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+VERSION？ | OK ＋VERSION:<version> | Firmware version |

### Inquire remote BT address

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+ RADDR? | OK ＋RADDR:<bdaddr> | Max connected BT device is 7 |

### Inquire local device BT address

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+LADDR？ | OK ＋LADDR:<bdaddr> | Bdaddr: is the BT address of the local module |

### Soft-reboot of the module

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+ RESTART | OK |  |

### Commence Discovery process

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+INQ | OK Inquiry result: +INQRESU:<bdaddr>, <name> Inquiry complete： +INQCOMP | < bdaddr >BT address of the discovered Bluetooth device < name > Friendly name of the discovered Bluetooth device. (note:If a name is not found then “Unknown” is returned) |

### Cancel the discovery process

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CANCEL | OK |  |

### Set/ Inquire PIN code mode

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+PINMODE=<flag> | OK | <flag>： 1: Use default PIN Response（doesn’t not send PINRES command） 0: Send PINRES Command） Default：0 |
| AT+PINMODE? | OK +PINMODE:<flag> | Pinmode Inquiry |

### Set /Inquire PIN (password) number

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+PASSWORD=<pin> | OK | <pin>：PIN number Default：0000 |
| AT+PASSWORD? | OK +PASSWORD:<pin> | <pin>: returns the current PIN # |

### Pair with remote Bluetooth Device

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+PAIR=<bdaddr> | OK | <bdaddr>Bluetooth Address <pin>PasswordPassword <Status> l: Success 0: Failure |
|  | +PININD: <bdaddr> |  |
| AT+PINRES=<bdaddr>,<pin> |  |  |
|  | +PAIR: <bdaddr>, <Status> |  |

### Unpair a remote device that is currenlty paired.

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+DEL=<bdaddr> | OK | <bdaddr> |

### Connect Remote Bluetooth device

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CONN=<bdaddr>, <service> | OK | <bdaddr>Blue tooth address <service> Device type 0x1101 SPP 0x1108 Headset |
|  | +CONN:<handle>,<bdaddr>, <service>,<state> | <handle>device ID Note: This device ID will be assigned after successful connection <bdaddr> <service>Device type <Status> : 0: Successfully connected 1: Can’t make connection/interrupted 2: Can’t not obtained Bluetooth device service type 3: Can’t pair |

### Disconnect Remote Bluetooth Device

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+DISC=<handle> | OK | <handle>Device ID |
|  | +CONN:<handle>,<bdaddr>, <service>,<state> | <handle> the device ID only will be signed after successful connection <bdaddr> BDADDRESS <service> Device Type <status>： 0: Successfully connected 1: Can’t make connection/interrupted 2: Can’t not obtained Bluetooth device service type 3: Can’t pair |

### Inquire Current Connection status

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+CONN? | OK +CONN: handle>,<bdaddr>, <service>,<status> | None Return current status. |

### Mode switch

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+MASTER=switch_mode | OK | switch_mode： 0 no Change 1: Switch to Master. If cannot switch to master, disconnect from remote device 2: Switch to Master, If cannot make the switch, stay connected Default = 2 |
| AT+MASTER? | OK +MASTER: switch_mode | Current status。 |

### LED operational Mode indicators

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+LED=spp_ind | OK | spp_ind: SPP（0-11）Connection LED indicating lamp disposition. (0-11) |
| AT+LED? | OK +LED: spp_ind |  |

### Module start instruction

| Command | Response from Module | Parameter |
| --- | --- | --- |
| AT+OPEN：paired_num | NONE | paired_num: Report connected number of devices |

### Inquire available AT instructions

| Command | Response from Module | Parameter |
| --- | --- | --- |
| ATZ? | OK List then available AT instructions | None |

## Data packet Format（0x10）

The data packet is formatted as follows:

- The first three bytes are fixed

- The next two bytes are indicative of the packet length

- The next two bytes are the destination header

- The remainder is the payload data which is two bytes less than the designated length

The following is an example of the Data communication format

| Fixed Header | Designator for data | Data length | Destination ID | Data |
| --- | --- | --- | --- | --- |
| 0x55 | 0xAA | 0x10 | Data length (2 bytes) | （2bytes) | application payload (length – 2bytes） |

The first three bytes are fixed as:  0x55 0xAA 0x10

The data length of two bytes includes the two bytes it needs to define the destination ID.

The Destination ID: 2 bytes in length and is returned when the device connects to a remote Bluetooth device. The destination ID is used to determine which device in the Piconet will receive the data.

Payload: this is the application data. The length of the data packet is its length reduce from the transmit length by two (2) bytes.

For example:

After connecting successfully, the module returns :

+CONN:1232,4A494E000067,1101,0

The connection destination ID is the 4A494E000067

The remote BT device corresponds to the 1232 (16 bits address)

If you choose to transmit the string of characters “HelloWorld” to the address is the 4A494E000067 equipment:

Then you will transmit “55 AA 10 00 0C 12 32 48 65 6C 6C 6F 57 6F 72 6C 64”

The data in Black = 55 AA 10 00 0C is the prefix and the data length (0x0C is the length)

The data in Blue = 12 32 is the destination ID

The data in Red = 48 65 6C 6C 6F 57 6F 72 6C 64 is Hello World

Please note: When transmitting large amounts of Data it is recommended that the system use Hardware Handshaking. This will help insure the reliability of the data in the Piconet. If for some reason hardware handshaking cannot be implemented the we recommend that the payload be limited to 400 bytes of data, Additionally  the data transmitting microprocessor should wait for an acknowledgement that the data was received properly before transmitting the next batch.

## Data packet reply (0x20)

The Reply to receiving a data packet is described below the receive data packet is distinguished by the 0x20 in the third byte position

| 0x55 | 0xAA | 0x20 | Data Length | Object code (1 byte | Destination ID (2 bytes) |
| --- | --- | --- | --- | --- | --- |

Object code Table

| Object code | Result description |
| --- | --- |
| 0x00 | Correct reply |
| 0x01 | Data packet error: Undefined packet type. |
| 0x02 | Packet length invalid (2<= N <=65535） |
| 0x03 | Data packet transmission time surpasses for 5 seconds |
| 0x04 | Invalid destination ID: If the Module receives a Data packet without a destination ID then the module will automatically substitute a default value of “00” |

If returns = 55 AA 20 00 03 04 12 34 then the 0x04 in the object code location is indicative of the fact that the Destination ID 1234 is invalid.

# How to connect to other SPP Bluetooth device

Red is from uP to Module, Blue is from Module to uP. Commands have to have header 0x55,0xAA, command ID (0x00), data length

Example:

AT+INQ<CR><LF>

| 55 AA | 00 | 00 08 | 41 54 2B 49 4E 51 0D 0A |
| --- | --- | --- | --- |
| Header | Command ID | Data Length | Command + CR and LF ( AT+INQ<CR><LF>) |

The complete data send from uP to Module are (Hex format)

55 AA 00 00 08 41 54 2B 49 4E 51 0D 0A

Bluetooth Module Discovery Inquiry

AT+INQ<CR><LF>

<CR><LF>OK<CR><LF>

Example: There is one Bluetooth devices address as 001B3502BC8B, name as ZBA-SPP

<CR><LF>+INQRESU:001B3502BC8B,ZBA-SPP<CR><LF>

if there is another Bluetooth devices address as 001B3502BC8A, name as ZBA-SPP

<CR><LF>+INQRESU:001B3502BC8A,ZBA-SPP<CR><LF>

Note the uP can cancel the discovery process at any time by send

(AT+CANCEL<CR><LF>)

<CR><LF>OK<CR><LF>

After completion of recovery

<CR><LF>+INQCOMP<CR><LF>

Pair the remote Bluetooth device

AT+PAIR=001B3502BC8B<CR><LF>

<CR><LF>OK<CR><LF>)

<CR><LF> +PININD: 001B3502BC8B<CR><LF>

AT+PINRES=001B3502BC8B,1111 <CR><LF>

(1111 is password of the remote Bluetooth device)

<CR><LF>OK CR><LF>

if Successfully paired

<CR><LF> +PAIR: 001B3502BC8B,1 <CR><LF>

Connect to SPP Bluetooth device

AT+CONN=001B3502BC8B,1101<CR><LF>

<CR><LF>OK<CR><LF>

Upon successfully connected

<CR><LF>+CONN:1232,001B3502BC8B,1101,0<CR><LF>

Note: 1232 is handle ID. You have to use this ID to communicate with this device.

After connection, the master and slave are ready to send data.

## 5. Serial port data transmission flow

### Transmitting Data

This example makes the assumption that the slave Bluetooth Handle ID is 0x1232

uP to Master module

(HelloWorld)

55 AA 10 00 0C 12 32 48 65 6C 6C 6F 57 6F 72 6C 64

55 AA 20 00 03 12 32

Slave Bluetooth device with ID 1232 will receive (HelloWorld) 48 65 6C 6C 6F 57 6F 72 6C 64

Slave to Master: (Slave device handle ID is 0x1232)

A (0x41)

The master module to uP

55 AA 10 00 03  0x1232 0x41

### Disconnecting serial port service

AT+DISC=1232 <CR><LF>

<CR><LF>OK<CR><LF>

(<CR><LF>+CONN=1010,001B3502BC8B,1101,1<CR><LF>)

# Bluetooth Module Hardware Specification

The multipoint Bluetooth module can be used with the following modules

- BT44-191C Data communication only

- BT44-191S Data and Audio

- BT44-147 Data and Audio

- BT44-111S Data and Audio

>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>